Motor encoder disks
1. Cut 25 mm strips from material.
2. Cut 25 mm x 25 mm squares from material (6 off).
3. Make two stacks of 3 squares, stacking with double-sided tape (one working stack, one for spacing).
4. Cover top of working stack with permanent marker.
5. Find centre of working stack and mark with pin.
6. Draw circles on working stack with compass with pin: 11.25 mm radius and 10.00 mm radius.
7. Push pin through centre of working stack (1 mm stick-out).
8. Put double-sided tape on bottom of working stack.
9. Align working stack on template using pin for centring.
10. Attach working stack to template with pre-placed double-sided tape.
11. Stick spacing stack to back of steel rule.
12. Mark hole centres on working stack: one end of steel rule against pin in centre of working stack, other end against knife or pin aligned in template, mark centre with knife, then mark centre with pin.
13. Remove template and centre pin from working stack and stick working stack to waste.
14. Drill circle of holes (1 mm) through working stack using pin marks for placement.
15. Drill centre hole (1.5 mm) through working stack.
16. Remove working stack from backing waste.
17. Hand sand outer profile of working stack to within 0.5 mm.
18. Tape working stack to 1.5 mm drill bit and use drill to rotary sand working stack to size and circularity.
19. Disassemble working stack and clean up encoder disks.